## Slide 1: Algorithm 2
Learning of the associative layer

## Slide 2: Flow Chart
Input – key and response vector
Memory Layer Training
Associative layer
Class Name
Connect node with arrow head
Add new node to associative layer represent new class
yes
No
Build an arrow edge between the key class and response class

## Slide 3: Finite State Machine
S0
Idle State
S4
Update existing node
S5
increment total input counter
S1
Memory training layer
S2
Check if class label cx exists
S3
Add new node
S6
connection between nodes b and d
Input vector
ML_training_done
No
Yes
Done
odd value
Even value

## Slide 4: S0: Idle state
Idle state : The FSM waits for each new input to arrive. When input arrives, transition to S1.
Note: For associative memory, new inputs arrive in pairs (b,d) sequentially.
We need a global input counter accessible from all states to keep track of the number of inputs we have processed.
The even/odd values of this counter distinguish between b/d type nodes.

## Slide 5: S1: Use algorithm 1 to train the memory layer
This is the state where we use algorithm 1 to train the memory layer (ML).
Controller issues a signal to read the image pattern x from memory.
When the ML finishes training as per algorithm1 (i.e. the correct class for x is identified and a node identified within the class to represent x, weights adjusted etc.), it raises a “ML_training_done" indication.
This triggers the transition to S2.
Note: S1 will have to fork off to another state machine to finish algorithm 1.

## Slide 6: S2: Cx exists in the list of classes in the associative layer (AL)
Check if class label cx exists in the list of classes in the associative layer (AL). Each class is represented by a single node in the AL.
If no node b exists in this list with a class label cx, then enter S3 and insert a new node b.
Implementation: Use a memory. Suppose, we expect a maximum of 10 classes. Use a 4 bit address as your class label. The content of this address should be a data structure which has a valid bit, indicating that the class exists in the AL. Add additional bits to the data structure to represent all the needed information.
Additional bits needed: Refer to Table 3 in the paper. Use only the first 4 elements of the table. RCi will be an array, because there can be multiple response classes for each class.

## Slide 7: S2..(continued)
When a new class label is presented, we check the memory with the class label as address. Check if the valid bit for the data at this address == 1. Else, we need to add a new node. So, transition to S3.
If node exists in the AL, transition to state S4.
Eg: addr = Cx
if (memory[addr].valid == 1)
next_state = S4; //update an existing node
else
next_state = S3; // add a new node

## Slide 8: S3: Insert a new node into associative memory
Insert a new node into the memory described in S2.
Use the class label as your address and the node struct as the data for this address.
When done, transition to S5
Addr = Cx;
memory[addr].valid = 1;
memory[addr].mi = 0; // Associative index mb (or md) = 0.
memory[addr].weight = node_value ;

## Slide 9: S4: Update the contents of node in AL
Node exists in memory. i.e. memory[addr].valid == 1, where addr = class label.
Update the contents of this node.
Increment the associative index of the node only if it is a “b” type node and not a “d” type node.
This can be identified by looking at the current node count. If the node count is even, it is a “b” node.
memory[addr].mi = memory[addr].mi + 1 ; //incrementing associative index
memory[addr].RC array cannot be updated yet, because we don’t know the class label cy for the response node (d).
Look up the memory layer (ML) from algorithm 1 to find the subnetwork of cx. For each node in the subnetwork, extract the Mi (number of connections of each node or how many times it was the winner. Also denoted as Ms1 in algorithm 1). Find the node with the max Mi. Use the weight of this "frequent winner" node (lets call it Wi)as the weight of the node b representing the class in the AL.
memory[addr].Wi = Wi
Store away the class label of b in a temporary storage, so that it can be used to make a connection with node d in S5.
Eg:
Temp_b = 4’b1110; // This temp_b gets updated every time we process a “b” type node.
Or
Temp_d = 4’b0100; // This temp_d gets updated every time we process a “d” type node.

## Slide 10: S5 : increment global input counter
In this stage, we increment the total input counter. For associative memory, new inputs arrive in pairs (b,d) sequentially.
If the input we just processed was of type “b”, the input counter will now have an odd numbered value. If so, jump to S0 to wait for the paired input “d”.
If the input we just processed was of type “d”, the input counter will now have an even numbered value. If so, jump to S6, where we make a connection between b and d.
Note: even/odd detection is just checking for (bit 0 == 0)

## Slide 11: S6 : Connection between nodes b and d
We make the connection between nodes b and d. Use the previously stored temp memory to retrieve class labels of cx and cy corresponding to b and d.
Iterate over all entries in the connection table. See if a pair (b,d) exists. If so, increment its weight.
Implementation: Use a lookup table. Use concatenation of the 4-bit values of cx and cy as a 8-bit key to look up the table. If a match is found, increment the weight corresponding to that 8-bit key.
Eg:
Temp_b = 4’b1110
Temp_d = 4’b0100
Hence key = 8’b11100100 = decimal 228
Connection_table[228] = Connection_table[228] + 1;
So a value of 0 indicates that no connection exists. A value > 0 indicates a connection (or “arrow”) between nodes b and d.

## Slide 12: S6..(continued)
We now update memory[addr].RC array mentioned in S4.
This is where a response class is added for each node.
Since RCb[mb] = Cd,
memory[addr].RC[mb] = Cd
Where addr = class label Cb

## Slide 13: Modules implemented in Memristor
N-bit Adder
Equality Comparator
And Gate

## Slide 14: Architecture
Associative Layer
Class Node Cx
Global Counter
Ci - Class name of node
Mi - Associative index of node
Wi - Weight of node
RCi- Response classes of node
Cb/Cd
Comparator for valid bit for given Cx address
Cx from ML
Cx from associative layer
Mux
Update Node
Mi = mi + 1
Addr = Cx
Mem[addr].valid=1
Mi = 0
Wt = node_value
Add New node
CbCd | Wt
C0C1 | 0
C0C2 | 2
Connection table
Ram Memory
N Bit adder
Comparator for connection table WT

## Slide 15: Contribution
Hiral Barot - Designed FSM logic and integrated Ram memory and connection table for node data update , test bench to simulate and check the state transitions after integration of memory and connection table for each node.
Jyothi – Struct definition in System Verilog and help with FSM logic, need to integrate memristive modules in place of combinational logic
Michael – Designed Ram memory and connection table
Hai dang - 4 bit greater than comparator pending
Manjith – Helped to understand the algorithm and FSM machine